## Slide 1
AirDrums
Roi Hirsch, Ori Chayoot, Gal Lifshitz, Asaf Manor
Advisor: Dr. Tammy Riklin Raviv
BACKGROUND
AirDrums is our concluding project in the Digital Image Processing (DIP) course in the Dept. of Electrical and Computer Engineering at Ben Gurion University. We have created a virtual drum kit, in which a player uses a pair of sticks with colored tips to hit virtual drums, while matching drum kit sounds are played. We use a pair of cameras located above the player facing downwards, capturing stereo images which are used for estimating the sticks’ spatial location and motion.
THE REQUIREMENTS
Detecting the spatial location of a tips of drum-sticks requires three complementary procedures:
Detecting and Tracking the locations of the tips in the image plane (multiple object tracking).
Calculating the distance to the tip from the cameras using passive Stereo Vision.
Estimating the sticks’ motion and deciding if, and which, a hit was made.
TECHNICAL CHALLANGES
Maximizing Frames per Second to allow Live play
The Frames per Second ratio (FPS) is bounded by three major constraints:
Rectification of the image pair – the process of projecting the images into a common image plane so that the shift, or disparity, could be detected and the distance could be estimated.
Conversion of the RGB acquired image pairs to a chosen color-space in which the sticks tip are easily detected.
Hardware constraints – Image acquisition rate constrained by the cameras, and image processing rate constrained by the computer and chosen implementation.
SOLUTIONS
We chose to tackle some of the challenges by the following optimizations:
Taking use of Epipolar Geometry, the detection of a tip of the stick in a matching stereo image can be restricted to an horizontal line corresponding to the height of the tip located in the first image.
The choice of color space used for detection takes into account the computational complexity of the conversion.
Although most of the implementation was done in the MATLAB prototyping language, the program makes use of pre-compiled modules from the OpenCV libraries.
The System